## Slide 1
B.TECH ME • 6TH SEMESTER
Session Jan – May 2026
Product Cycle and CAD Systems
Computer Aided Design Lecture 1 Module 1
PREPARED BY
Dinesh Kumar
Assistant Professor
D Y PATIL INTERNATIONAL UNIVERSITY
School of Continuing Education

## Slide 2
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
02
Learning Objectives
& Course Agenda
Understand the complete product cycle from concept to End-of-Life (EOL)
Master design processes, engineering methodologies, and CAD systems
Explore CAD architecture, hardware components, and system integration
Derive and apply 2D/3D transformations and coordinate systems
COURSE PROGRESSION
Product Lifecycle
Concurrent Eng.
CAD Systems
Graphics Basics
3D Transforms

## Slide 3
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
03
Lifecycle Phases
Key Stage Gates
Product Cycle
End-to-End Overview
KEY PERFORMANCE INDICATORS
Time-to-Market
Cost
Quality
Reliability
Sustainability
Opportunity: Market needs & VOC
Concept & Design: R&D, Prototyping
Manufacturing: Production ramp-up
Use & Service: Maintenance & Updates
EOL: Recycle, Remanufacture, Dispose
Feasibility: Technical & Economic check
Design Freeze: Specs locked for tooling
Pilot Run: Validation of process
Launch: Full scale commercialization

## Slide 4
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
04
Product Lifecycle
PHASES & GOVERNANCE
1. Concept Phase
Analyze market needs, capture Voice of Customer (VOC), and perform competitive analysis. Output: Product Mission Statement.
2. Development Phase
System design, detailed engineering, prototyping, and validation (V-Model). Defining requirements and constraints.
3. Production Phase
Manufacturing ramp-up, Supply chain setup, SPC (Statistical Process Control), and PPAP (Production Part Approval Process).
4. In-Service Phase
Distribution, customer use, maintenance, software updates, and field data collection for future improvements.
5. End of Life (EOL)
Product retirement, remanufacturing, recycling, and ensuring regulatory compliance (e.g., WEEE, RoHS).
STAGE-GATE GOVERNANCE MODEL
Gate 1: Feasibility
Gate 2: Design Freeze
Gate 3: Launch Approval
Concept
Market & Tech Assessment
Design
Prototyping & Testing
Pilot
Mfg Process Validation
Launch & Sustain
Mass Production

## Slide 5
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
05
Systematic Steps
Key Methodologies
Design Process
From Problem to Solution
Morphological Charts
Pugh Matrix
TRIZ
Rapid Prototyping
Brainstorming
SCAMPER
Definition: Problem statement & goals
Requirements: Functional specs & constraints
Concept: Brainstorming & Generation
Selection: Evaluation (Pugh Matrix)
Embodiment: Architecture & Preliminary layout
Detail Design: Technical drawings & specs
V&V: Verification & Validation

## Slide 6
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
06
Methodologies for Quality, Manufacturability, and Reliability
WHATs
Relationship Matrix
HOWs
Design Methods
QFD
Quality Function Deployment
House of Quality
DFM / DFA
Design for Mfg / Assembly
Complex
Simplified
FMEA
Failure Mode & Effect Analysis
RPN = S × O × D
Risk Priority Number
Low Risk
Medium
High Risk
Translates "Voice of Customer" (VOC) into engineering specs (CTQs).
Uses "House of Quality" matrix to correlate needs vs. features.
Prioritizes design requirements based on customer value.
DFM: Optimize part manufacturing (tolerances, materials).
DFA: Minimize part count, standardize fasteners, ease of handling.
Reduces production cost and assembly time.
Part Count Reduction
Identify potential failures before they occur.
RPN Calculation:Severity × Occurrence × Detection
Focuses mitigation on high RPN items (Safety/Reliability).

## Slide 7
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
Characteristics
Advantages
Limitations
Sequential Engineering
Traditional "Over-the-Wall" Approach
Linear Process: Strict order of phases
Siloed Teams: Limited communication
Handoffs: Completed work passed blindly
Late Validation: Testing only at the end
Clear ownership & accountability
Simpler project management
Well-defined milestones
Long time-to-market
Late discovery of design defects
Expensive rework cycles
Poor design-for-manufacturing fit
Concept

## Slide 8
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
08
Parallel Workflows vs. Traditional Sequential Handoffs
Concurrent Engineering
Sequential
Traditional "Over-the-Wall"
Concurrent
Integrated Product Dev
Impact
Why Switch?
Linear workflow: Design → Mfg → Test.
Late discovery of defects leads to costly rework.
Siloed teams with minimal communication.
Concept
Design
Mfg
Rework
Long Lead Time
Parallel execution of phases (overlap).
Cross-functional teams (Design, Mfg, Mkt).
Early supplier involvement & feedback.
Concept
Design
Mfg Planning
Production
Collaboration
Speed: 30-50% reduced time-to-market.
Cost: Fewer Engineering Change Orders (ECOs).
Quality: Design for Manufacturability (DFM) built-in.
100%
Sequential
-40%
Concurrent
Time & Cost

## Slide 9
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
09
CAD Systems
INTRODUCTION, EVOLUTION & APPLICATIONS
Evolution of CAD
Transitioned from simple 2D electronic drafting to complex 3D Parametric Solid Modeling, and now to Model-Based Definition (MBD) where 3D models carry all PMI data.
Key Applications
Used extensively for Part & Assembly Design, Complex Surfacing, Simulation Pre-processing (FEA/CFD), and Tooling Design (Molds/Dies).
Parametric & Feature-Based
Modern CAD uses constraints, dimensions, and relations. Design intent is captured through a history-based feature tree, allowing easy updates.
Role in Product Cycle
Acts as the central source of truth for the "Digital Thread," feeding data downstream to CAM, CAE, and quality inspection.
VISUAL PROGRESSION: 2D TO MBD
1
2D Drafting
Electronic drawing board, lines & arcs.
2
3D Solid Modeling
Wireframe → Surface → Solid geometry.
3
Parametric Feature-Based
History tree, constraints, associativity.
4
MBD / PMI
3D Annotated Models (No 2D drawings).
CORE BENEFITS
Precision
Associativity
Collaboration
Reuse

## Slide 10
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
10
Workflow Pipeline
System Interoperability
CAD Workflow
Digital Thread Integration
NEUTRAL FORMATS
STEP
IGES
JT
Parasolid
Input: Problem Definition & Requirements
Modeling: Parametric 3D CAD Creation
Management: PDM Check-in / Version Control
Output: BOM Generation & 2D Drawings
Downstream: CAM Toolpaths & CAE Sim
Core Integration: PLM, ERP, CAM, CAE
Change Control: Revision Mgmt & ECOs

## Slide 11
CAD Hardware
WORKSTATION ARCHITECTURE & REQUIREMENTS
Processor (CPU)
High clock speed (>4.0 GHz) is crucial for parametric modeling (linear). Multi-core helps with rendering and simulation.
Rec: Intel Core i9/Xeon or AMD Ryzen 9
Graphics (GPU)
Professional cards offer certified drivers for stability and ECC VRAM. Handles viewport rotation and shading.
Rec: NVIDIA RTX A-Series / Quadro (≥ 8GB VRAM)
Memory (RAM)
Holds full assembly data in active memory. Prevents swapping to disk which kills performance.
Rec: 32GB (Entry) - 64GB+ (Complex Assemblies)
Storage & I/O
Fast loading of large assemblies. High-res display for detail.
Rec: NVMe SSD (Gen4/5), 4K IPS Monitor, SpaceMouse
WORKSTATION PERFORMANCE STACK
DATA BUS (PCIe / DDR)
HIGH SPEED STORAGE FABRIC
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
11
Display I/O
4K Color Accurate
Input Devices
3D Mouse / Tablet
CPU
Geometry Engine
GPU
Viewport Rendering
System RAM
Active Workspace
NVMe Storage
File Repository

## Slide 12
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
12
CAD System Architecture
Software Kernel & Geometry Mathematics
B-Rep (Boundary Rep)
Object defined by topological limits: Vertices, Edges, Faces. Uses Euler-Poincaré Formula: V - E + F = 2 (for simple convex polyhedra).
CSG (Constructive Solid)
Object constructed via Boolean operations (Union ∪, Intersection ∩, Difference -) on primitives like spheres, cubes, cylinders.
Software Architecture
Graphics Engine (OpenGL/DirectX)
Data Structures
Half-Edge Structure: Efficient for mesh traversal.
Scene Graph: Hierarchical arrangement of assembly components.
Octree/BSP: Spatial partitioning for collision detection.
User Interface (GUI)
Application Logic
Feature Manager, Constraints
Geometric Kernel
Parasolid
ACIS

## Slide 13
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
13
Raster: Grid of pixels (Bitmap, JPEG). Resolution dependent. Good for complex textures/photos.
Vector: Geometric primitives (Lines, Curves). Infinite scaling without quality loss. Used in CAD.
Frame Buffer: Stores final color values (RGBA).
Z-Buffer (Depth): Stores depth (distance) to handle object occlusion.
Stencil Buffer: Limits rendering area (masking/clipping).
Flat: One color per polygon face (blocky).
Gouraud: Vertex lighting interpolated across face (smooth, no specular).
Phong: Normal interpolation per pixel (high quality specular highlights).
Computer Graphics
FUNDAMENTALS & PIPELINE
Raster vs. Vector
Two fundamental ways to represent 2D images.
Graphics Buffers
Memory areas storing data for each pixel on the screen.
Shading Models
Methods to calculate light intensity on surfaces.
THE RENDERING PIPELINE
1
Model & World Transform
Object Coords → World Space
2
Viewing & Projection
Camera Space → Clip Space (Frustum)
3
Rasterization
Primitives → Fragments (Pixels)
4
Fragment Processing
Shading, Texturing, Depth Test
5
Display
Frame Buffer → Screen

## Slide 14
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
14
Coordinate Systems
Conversions and Mathematical Definitions
System Visualization
Visual comparison of reference frames and basis vectors
Key Applications
Spherical: Camera rotations, environment mapping, orbital mechanics.
Cylindrical: Modeling shafts, pipes, and rotational symmetry objects.
Homogeneous Coords: Unified handling of translation and rotation (essential for 3D matrices).
Convention Note
In graphics (OpenGL), Y often points up. In physics/engineering, Z often points up. Always verify the "up" vector and handedness.

## Slide 15
15
2D Transformations
Homogeneous Matrix Operations (3×3)
Step-by-step transformation: Original → Translate → Rotate → Scale
Composite Transformations
Matrix multiplication is non-commutative ($A \cdot B \neq B \cdot A$). Order matters!
M = T · R · S
(Scale first, then Rotate, then Translate)
Why Homogeneous?
Unifies Translation (addition) with Rotation/Scaling (multiplication) into a single matrix format.
Allows chaining multiple transforms via matrix multiplication.

## Slide 16
3D Transformations
Homogeneous Coordinates (4×4 Matrices)
Visualizing Rotations
The diagram demonstrates rotations around the three principal axes. Note that in a right-handed system, positive rotation is counter-clockwise when looking towards the origin from the positive axis.

## Slide 17
17
Projection & Viewing
Camera Models & Transformation Matrices
Projection Types
Perspective
Objects appear smaller as they get further away. Parallel lines converge at vanishing points. Mimics human vision.
Orthographic
Parallel projection. No depth perception scaling. Essential for engineering drawings and CAD measurements.
View Frustum
Volume visible to the camera (Truncated Pyramid)
Camera Transform
Transforms world coordinates to camera coords.
𝑃
𝑐
𝑎
𝑚
=
𝑅
⋅
(
𝑃
𝑤
𝑜
𝑟
𝑙
𝑑
−
𝐶
)

## Slide 18
B.Tech ME • 6th Semester • Product Cycle and CAD Systems
18
Advanced 3D Concepts
Viewing Pipeline & Precision
Transformation Pipeline Object → World → Camera → Clip → NDC → Screen Space sequence.
Clipping & Culling Discarding geometry outside frustum and back-facing polygons to optimize rendering.
Depth Precision (Z-Buffer) Non-linear distribution of depth values. Importance of Near/Far plane ratio to avoid Z-fighting.
Coordinate Conventions Right-handed (OpenGL) vs Left-handed (DirectX) systems affect matrix composition.
VIEWING PIPELINE
Object Space
World Space
Camera/View
Clip / NDC
Screen Space

## Slide 19
Prepared by:
Dinesh Kumar
| Assistant Professor
Session Jan – May 2026 | B.Tech ME
End-to-End Integration
Concurrent Efficiency
Digital Foundation
Mathematical Core
Summary
Key Takeaways & Conclusions
Product success relies on the seamless integration of design, manufacturing, and lifecycle management (PLM) from concept to disposal.
Shifting from sequential to concurrent engineering significantly reduces time-to-market and minimizes late-stage design changes.
CAD systems and geometric modeling are the backbone of modern engineering, enabling precise simulation and digital twin capabilities.
Mastery of coordinate systems and matrix transformations is essential for understanding 3D graphics, robotics, and advanced CAD operations.
Questions & Discussion
Thank you for your attention
Integrated Lifecycle Model