## Slide 1
DESIGN OF MACHINE ELEMENTS-I
BME 2201
Lecture 4 Module 1
Dinesh Kumar
Assistant Professor
School of Engineering
DYPIU

## Slide 2
MODES OF FAILURE
In engineering design, understanding modes of failure is crucial for ensuring the reliability and safety of machine elements.
1. Static Failure Modes:
Yielding: Occurs when the material undergoes plastic deformation under static loading conditions. This can lead to permanent deformation or fracture depending on the material properties.
Fracture: Sudden and catastrophic failure of a component due to excessive stress concentrations or flaws. Fractures can propagate rapidly through the material, leading to complete structural failure.
Buckling: Failure due to sudden bending or compression, causing the component to deform laterally or buckle. Buckling typically occurs in slender structures under compressive loads.

## Slide 3
MODES OF FAILURE
2. Fatigue Failure Modes:
Fatigue: Gradual and progressive failure of a material under cyclic loading. Over time, repeated cycles of stress can cause micro-cracks to initiate and propagate, eventually leading to failure, even at stresses below the material's yield strength.
Creep: Slow deformation of a material over time under a constant load or stress, particularly at elevated temperatures. Creep can cause components to elongate or deform, eventually leading to failure.

## Slide 4
MODES OF FAILURE
3. Dynamic Failure Modes:
Impact: Failure due to sudden and high-energy loading, such as impacts or collisions. Impact loading can induce stress concentrations and result in fractures or deformation.
Vibration Fatigue: Failure resulting from cyclic loading induced by vibrations. Vibrations can cause stress concentrations at specific points in a structure, leading to fatigue failure over time.

## Slide 5
4. Wear and Erosion:
Abrasive Wear: Occurs when hard particles or surfaces rub against softer materials, causing progressive material removal and surface degradation.
Adhesive Wear: Results from the transfer of material between sliding surfaces under high contact pressures. This can lead to surface roughening, increased friction, and eventual failure.
Erosion: Gradual removal of material due to the impact of abrasive particles, fluids, or gases. Erosion can weaken components and compromise their structural integrity over time.
MODES OF FAILURE

## Slide 6
MODES OF FAILURE
Corrosion:
Galvanic Corrosion: Electrochemical process where two dissimilar metals come into contact in the presence of an electrolyte, leading to accelerated corrosion of one of the metals.
Pitting Corrosion: Localized corrosion characterized by the formation of small pits or craters on the surface of a material, often caused by chemical reactions or exposure to corrosive environments.
Stress Corrosion Cracking: Occurs when a material is subjected to both tensile stress and a corrosive environment, leading to the propagation of cracks and eventual failure.

## Slide 7
FACTOR OF SAFETY
Factor of Safety:
The ratio of maximum stress to working stress is called as factor of safety.
Factors for Selection of Factor of Safety:
Reliability of properties of material.
Change in the properties while service.
Reliability of applied load.
The certainty as to exact mode of failure.
The extent of loss of life.
Materials | Factor of Safety
Ductile | 
Brittle | 
Type of Load | Factor of Safety
Static | 1.5 to 3
Variable | 3 to 6
Impact | 6 to 12

## Slide 8
FACTOR OF SAFETY FOR BRITTLE MATERIALS
For brittle materials like ceramics or some types of concrete, failure occurs suddenly without significant deformation. The factor of safety for brittle materials is typically calculated using the following formula:
Where:
Ultimate Strength is the maximum stress the material can withstand before failure.
Working Stress is the maximum stress the material will experience during normal operation.
A factor of safety greater than 1 indicates a margin of safety between the applied stress and the ultimate strength of the material.

## Slide 9
FACTOR OF SAFETY FOR DUCTILE MATERIALS
For ductile materials like most metals, failure is characterized by significant deformation before rupture. The factor of safety for ductile materials typically accounts for yielding as well as ultimate failure. It can be calculated using the following formula:
Where:
Yield Strength is the stress at which the material begins to deform plastically (permanent deformation).
Applied Stress is the maximum stress the material will experience during normal operation.
A higher factor of safety provides greater assurance of safety but may result in increased material usage and cost.

## Slide 10
SELECTION OF MATERIAL
4. MANUFACTURING CONSIDERATIONS
In some applications, machinability of material is an important consideration in selection. Sometimes, an expensive material is more economical than a low priced one, which is difficult to machine. Free cutting steels have excellent machinability, which is an important factor in their selection for high strength bolts, axles and shafts. Where the product is of complex shape, castability or ability of the molten metal to flow into intricate passages is the criterion of material selection.

## Slide 11
SELECTION OF MATERIAL
Selecting the right material is crucial in machine design, balancing performance and cost. It's a complex process often involving trial and error. Key factors in material selection include mechanical properties, such as strength and toughness, as well as factors like corrosion resistance and thermal conductivity. Careful consideration of these factors ensures optimal performance and reliability of machine components. The factors which should be considered while selecting the material for a machine component are as follows:

## Slide 12
SELECTION OF MATERIAL
1. AVAILABILITY
Availability of materials is crucial in machine design, ensuring a consistent supply for production. Materials like cast iron and aluminum alloys are typically abundant and readily accessible. However, shortages of materials such as lead and copper alloys are common, posing challenges for manufacturing. Engineers must consider material availability to avoid production delays and disruptions. Strategies like diversifying material sources or substituting with more readily available alternatives may be necessary to mitigate supply chain risks. Balancing material availability with desired properties is essential for efficient and reliable machine design and production.

## Slide 13
SELECTION OF MATERIAL
2. COST
Cost For every application, there is a limiting cost beyond which the designer cannot go. When this limit is exceeded, the designer has to consider other alternative materials. In cost analysis, there are two factors, namely, cost of material and the cost of processing the material into finished goods. It is likely that the cost of material might be low, but the processing may involve costly manufacturing operations.

## Slide 14
SELECTION OF MATERIAL
3. MECHANICAL PROPERTIES
Mechanical properties are crucial in material selection for machines, encompassing factors like strength, elasticity, and hardness. Different applications demand specific properties; for instance, connecting rods require endurance against fluctuating stresses, while piston rings need hardness for wear resistance. Bearings benefit from low friction, whereas clutch linings necessitate high friction coefficients. Materials for automobile bodies should exhibit plasticity to withstand deformation without breaking. Understanding these properties guides engineers in choosing materials suited to each component's functional requirements.