## Slide 1
ENGINEERING SCIENCES
(BME 2105)
Dinesh Kumar
Assistant Professor
School of Engineering

## Slide 2
ADVANTAGES AND LIMITATIONS:
Advantages:
  NiMH batteries have higher energy density compared to Nickel-Cadmium (NiCd) batteries.
  They are more environmentally friendly due to the absence of toxic cadmium.
  NiMH batteries are relatively inexpensive and have better capacity retention than NiCd batteries.

## Slide 3
Limitations:
They are prone to self-discharge, losing charge even when not in use.
NiMH batteries exhibit a lower self-life compared to some other rechargeable batteries.
Their energy density is lower compared to lithium-ion batteries, limiting their use in high-demand applications like electric vehicles.

## Slide 4
CHARGING REACTION:
Cathode:
Ni(OH)2 → NiOOH + H2O + e−
The nickel hydroxide (Ni(OH)2​) at the cathode undergoes oxidation, releasing oxygen ions and accepting electrons, transforming into nickel oxyhydroxide (NiOOH).
Anode:
MH + H2O + e− → M + OH−
The metal hydride compound (MH) in the anode releases hydrogen ions (H⁺) and electrons (e⁻), reverting back to its original metal state (M) while forming hydroxide ions (OH−).

## Slide 5
DISCHARGING REACTION:
Cathode:
NiOOH + H2O + e− → Ni(OH)2
The nickel oxyhydroxide (NiOOH) at the cathode reacts with water and electrons from the anode, converting back to nickel hydroxide (Ni(OH)2).
Anode:
M + OH− → MH + H2O + e−
The metal (M) in the anode reacts with hydroxide ions (OH−) and captures electrons (e⁻), reforming the metal hydride (MH) and generating water.

## Slide 6
SOLID STATE ELECTROLYTES
Solid-state electrolytes replace the liquid or gel electrolytes found in conventional batteries with solid materials that conduct ions. They serve as the medium through which ions travel between the cathode and anode, enabling the flow of charge during the battery's charge and discharge cycles.

## Slide 7
Types of Solid-State Electrolytes
Ceramic-Based Electrolytes
Polymer-Based Electrolytes
Composite Electrolytes

## Slide 8
CERAMIC-BASED ELECTROLYTES:
Ceramic electrolytes are crystalline materials, often composed of lithium, sodium, or other alkali metals combined with oxides, sulfides, or phosphates. Examples include lithium phosphorus oxynitride (LiPON) and lithium garnet (LLZO).
These materials offer high ionic conductivity and stability, making them promising for high-energy and high-power applications. However, they can be brittle and challenging to manufacture in large quantities.

## Slide 9
POLYMER-BASED ELECTROLYTES:
Polymer electrolytes consist of polymer matrices infused with salts that facilitate ion conduction. They can be flexible and easier to process compared to ceramic alternatives.
Polymer electrolytes show potential for improved safety and flexibility in design. However, achieving high conductivity at room temperature remains a challenge.

## Slide 10
COMPOSITE ELECTROLYTES:
Composite electrolytes combine different types of solid materials, such as ceramics and polymers, to leverage their individual advantages. These hybrids aim to optimize both ionic conductivity and mechanical properties.
The goal is to create materials that exhibit higher conductivity while maintaining desirable mechanical characteristics, addressing the limitations of individual solid-state electrolyte types.

## Slide 11
ADVANTAGES OF SOLID-STATE ELECTROLYTES:
Improved Safety:
  Solid-state electrolytes are less prone to leakage and thermal runaway compared to liquid electrolytes, enhancing battery safety.
Higher Energy Density:
  Solid-state electrolytes enable the use of higher energy-dense materials and reduce the need for additional safety components, potentially increasing overall battery energy density.
Stability and Longevity:
  Solid-state electrolytes can offer improved chemical and electrochemical stability, potentially extending battery lifespan.
Flexibility in Design:
  Solid-state electrolytes allow for more flexible battery designs, potentially enabling thinner and more customizable shapes.