## Slide 1
ENGINEERING SCIENCES
(BME 2105)
LECTURE 21 MODULE 3
Dinesh Kumar
Assistant Professor
School of Engineering

## Slide 2
NANOMATERIALS USED FOR ENERGY STORAGE IN LITHIUM-ION BATTERY
1. GRAPHENE AND GRAPHENE OXIDE:
Graphene: Provides high electrical conductivity, large surface area, and mechanical strength, enhancing the battery's capacity and charge rate.
Graphene Oxide: Offers improved stability, higher surface area, and facilitates electrolyte stability, enhancing the overall performance and cycle life of the battery.
IMPROVEMENTS:
Enhanced Conductivity: Graphene's high electrical conductivity speeds up electron transport, improving the battery's charge and discharge rates.
Increased Stability: Graphene oxide enhances the battery's stability by mitigating electrode-electrolyte reactions, prolonging cycle life.

## Slide 3
2. CARBON NANOTUBES (CNTS):
Single-Walled Carbon Nanotubes (SWCNTs) and Multi-Walled Carbon Nanotubes (MWCNTs): Known for their exceptional mechanical strength, electrical conductivity, and high surface area, contributing to enhanced lithium storage and faster electron transport.
IMPROVEMENTS:
Enhanced Lithium Storage: CNTs' high surface area provides more active sites for lithium storage, increasing the battery's capacity.
Improved Conductivity: CNTs' excellent conductivity aids in efficient electron transport, enhancing charge and discharge rates.

## Slide 4
3. NANOSTRUCTURED SILICON (SI) AND SILICON NANOWIRES:
Silicon-based nanomaterials possess high theoretical specific capacity for lithium storage. However, they face challenges related to volume expansion during cycling, which Nano structuring helps mitigate, leading to improved capacity and cycling stability.
IMPROVEMENTS:
Enhanced Capacity: Nano structuring reduces volume expansion issues, allowing silicon-based materials to store more lithium ions, improving overall battery capacity.
Better Stability: Nanostructured forms mitigate mechanical stress during cycling, leading to improved stability and longer cycle life.

## Slide 5
4. METAL OXIDE NANOPARTICLES (E.G., TIO2, SNO2, FE2O3):
Metal oxide nanoparticles offer higher lithium storage capacities due to their unique crystal structures and high surface areas, providing promising alternatives to conventional graphite anodes.
IMPROVEMENTS:
Higher Lithium Storage: Metal oxide nanoparticles offer higher capacities due to their larger surface areas, increasing the overall energy storage capacity of the battery.
TiO2: Titanium dioxide
SnO2: Tin(IV) oxide or stannic oxide
Fe2O3: Iron(III) oxide or ferric oxide

## Slide 6
5. NANOSTRUCTURED SULFUR (S) AND SULFUR-COMPOSITE MATERIALS:
Nanostructured sulfur and sulfur-based composites can be used in cathodes due to their high theoretical capacity for lithium storage. Nano structuring helps overcome the issue of volume expansion and contraction during charge-discharge cycles, improving stability.
IMPROVEMENTS:
Higher Capacity: Nano structuring reduces volume changes, enhancing the stability of sulfur-based materials and increasing their lithium storage capacity.

## Slide 7
6. METAL SULPHIDES AND PHOSPHIDES:
Materials like metal sulphides (e.g., CoS2, FeS2) and metal phosphides (e.g., FeP, CoP) with nanostructured forms offer enhanced lithium storage capacity, stability, and conductivity, potentially serving as both anode and cathode materials.
IMPROVEMENTS:
Enhanced Capacity and Stability: Nanostructured metal sulphides/phosphides offer improved stability, higher capacity, and better conductivity, contributing to overall battery performance.
CoS2: Cobalt disulphide
FeS2: Iron disulphide or commonly known as pyrite
FeP: Iron phosphide
CoP: Cobalt phosphide

## Slide 8
7. HYBRID AND COMPOSITE NANOMATERIALS:
Combining different nanomaterials or integrating them into composites can harness synergistic effects, combining the unique properties of various nanoparticles to optimize battery performance, stability, and cyclability.
IMPROVEMENTS:
Synergistic Effects: Combinations of nanomaterials create synergistic effects, improving overall battery performance beyond what individual materials can achieve alone.
Tailored Properties: Composites allow tailoring of properties, such as improved conductivity, stability, and increased capacity, based on specific application needs.