## Slide 1
ENGINEERING SCIENCES
(BME 2105)
LECTURE 8 MODULE 2
Dinesh Kumar
Assistant Professor
School of Engineering

## Slide 2
CHEMISTRY FOR ELECTRIC POWER MOBILITY
ELECTRIC VEHICLES (EVS):
Electric vehicles are powered by electricity instead of internal combustion engines, reducing greenhouse gas emissions.
They use rechargeable batteries to store electrical energy for propulsion.
The key components of an EV include the battery pack, electric motor, power electronics, and a charger.
The electric motor converts electrical energy from the battery into mechanical energy to drive the vehicle.
Electric vehicles produce zero tailpipe emissions, reducing air pollution in urban areas.

## Slide 3
BATTERY CHEMISTRY:
Lithium-ion (Li-ion) batteries are the most common type used in EVs due to their high energy density and relatively long lifespan.
Li-ion batteries contain a cathode, anode, separator, and electrolyte to facilitate the flow of lithium ions during charging and discharging.
The cathode typically consists of lithium cobalt oxide (LiCoO2), lithium iron phosphate (LiFePO4), or other materials that can store and release lithium ions.
The anode is usually made of graphite or other carbon-based materials.
The electrolyte is a lithium salt dissolved in a solvent, allowing lithium ions to move between the cathode and anode.

## Slide 4
CHARGING AND DISCHARGING:
When an EV is plugged in for charging, electricity is supplied to the battery, causing lithium ions to move from the cathode to the anode, storing energy.
During discharge, when the vehicle is in use, the lithium ions return to the cathode, releasing stored energy and powering the electric motor.
The rate at which a battery can be charged and discharged is influenced by its chemistry and design, as well as temperature conditions.

## Slide 5
BATTERY MANAGEMENT AND SAFETY:
Battery management systems (BMS) monitor and control various parameters of the battery, such as voltage, temperature, and state of charge, to ensure safe and efficient operation.
Overcharging, overdischarging, and high temperatures can degrade battery performance and pose safety risks, so BMS systems help prevent these issues.
Cooling and thermal management systems are used to maintain the battery's temperature within safe limits during operation.

## Slide 6
ENERGY EFFICIENCY:
EVs are generally more energy-efficient than internal combustion engine vehicles, converting a higher percentage of the electrical energy into vehicle propulsion.
Regenerative braking systems in EVs capture and store energy during deceleration, improving overall efficiency by recycling energy that would be wasted in traditional vehicles.

## Slide 7
SUSTAINABILITY:
The environmental impact of electric mobility also depends on the source of electricity used for charging. Clean energy sources such as wind, solar, and hydroelectric power can significantly reduce the carbon footprint of electric vehicles.
Recycling and disposal of batteries are important for reducing their environmental impact, as they contain materials like lithium, cobalt, and nickel.

## Slide 8
1. BATTERY DEMANDING CRITERIA:
a. Energy Density: High energy density is crucial to store more energy in a compact and lightweight battery. This allows for longer driving ranges and lighter vehicle weight.
b. Power Density: High power density enables rapid acceleration and regenerative braking, improving overall vehicle performance.
c. Cycle Life: EV batteries need a long cycle life to maintain performance over many charge and discharge cycles, ensuring the durability of the vehicle.

## Slide 9
d. Fast Charging: Fast charging capability is essential for convenient recharging during long trips or when a quick charge is needed.
e. Safety: Battery systems must meet stringent safety criteria to protect against thermal runaway, overheating, and fire hazards.
f. Cost-Efficiency: Cost-effective production is vital to make EVs competitive with internal combustion engine vehicles.
g. Environmental Impact: Reducing the environmental impact of battery production is important, including the sourcing of raw materials and energy efficiency in manufacturing.

## Slide 10
2. SAFETY CONCERNS:
a. Thermal Runaway: One of the primary safety concerns is thermal runaway, which can lead to battery fires or explosions. It occurs when the battery overheats due to internal or external factors.
b. Overcharging and Overdischarging: Extreme overcharging or overdischarging can damage the battery, reduce its lifespan, and pose safety risks.
c. Puncture and Impact: Physical damage to the battery, such as punctures or impacts in accidents, can lead to short circuits and safety hazards.

## Slide 11
d. Cathode Materials: Some cathode materials, like lithium cobalt oxide (LiCoO2), can be less stable and more prone to thermal runaway compared to other materials like lithium iron phosphate (LiFePO4).
e. Cell Design: Proper cell design, including safety features like thermal management, pressure relief mechanisms, and separator materials, is essential to mitigate safety risks.
f. Recycling: Disposing of or recycling used EV batteries is an environmental and safety concern, as improper handling can lead to pollution or hazards.

## Slide 12
3. RECYCLING REQUIREMENTS:
a. Resource Conservation: Recycling EV batteries helps conserve valuable materials like lithium, cobalt, and nickel, reducing the need for new mining and lowering environmental impact.
b. Environmental Regulations: Recycling facilities must adhere to strict environmental regulations to handle and dispose of hazardous battery materials safely.
c. Collection and Transportation: Efficient collection and transportation systems are required to gather used batteries from various sources, including vehicle manufacturers and end-of-life vehicles.

## Slide 13
d. Battery Disassembly: The recycling process involves disassembling batteries, separating components, and extracting valuable materials.
e. Material Recovery: Recycling plants recover usable materials from old batteries through processes like hydrometallurgy, pyrometallurgy, and direct recycling.
f. Reuse: Whenever possible, used batteries that still meet safety and performance criteria can be refurbished and reused in other applications, reducing the demand for new batteries.
g. Disposal of Hazardous Waste: Any non-reusable battery components should be disposed of in accordance with environmental regulations, preventing pollution and protecting public health.